Notes on Parts

# 02_548_y-motor-bracket
Overhang to build surface on rear elongated motor bolt hole necessary?
Remove counter sinks
More bracing to hols motor secure.
Use easily accessible idler for tension rather than motor.
Groove bolt hole body could be taller to secure onto the rail better when tightened?
# 15_441_z-gear-driven
Needs to be built with brim.
# 16_492_z-bearing-clamp

(revised) Bolt boss 45 degree slope results in two sharp points trying to meet. Both curl away form intended position.
(revised) Use more of a slope from main body to boss to reduce overhangs.
(revised) Bearing centre to close to base of part.
# 18_440_z-gear
Needs to be built with brim.
# 20_446_extruder-small-gear
Needs to be built with brim.
# 21_xxx_retaining-tongue
No issues. Keying design to prevent incorrect orientation in assembly would help.
# 22_447_extruder-large-gear
Needs to be built with brim.
# 08_549_y-bearing-belt-clamp
Potentially need to lift bearing 0.1mm.
Belt too tight a fit in gripper.
# 09_550_y-bearing-clamp-tagged
Potentially need to lift bearing 0.1mm.