Ormerod 2 Documentation

# Ormerod 2
## Overview
The RepRap Pro Ormerod 2 is the latest RepRap self-replicating 3D printer from RepRap Pro. The machine is a faster to assemble, networked 3D printer with non-contact bed probe for full geometric compensation.
These pages are the complete instructions for building, commissioning and using the RepRapPro Ltd version of RepRap Ormerod 2. Like all RepRap machines, RepRapPro Ormerod 2 is fully open-source. It is licensed under the GPL. All the design files and software are available from the RepRapPro Ltd Github repository.
The RepRapPro Ormerod 2 is fitted with the open-source Duet electronics.
If you want to print the plastic parts for a RepRapPro Ormerod 2, see this web page.
## General Notes
BEFORE YOU ATTEMPT TO ASSEMBLE ANY PART OF THE RepRapPro ORMEROD 2 3D PRINTER, PLEASE READ THESE BUILD INSTRUCTIONS FULLY AND ENSURE YOU UNDERSTAND THEM. Although all parts are covered by warranty, this will be invalidated by your not following these build instructions. You are building a complicated machine; many different skills are required to build, to commission and to operate a 3D printer. Try not to rush your build, or you may miss out something vital!
- Give yourself plenty of space and ensure your work area is clean. Dust and dirt are a 3D printer’s worst enemy.
- All printed parts have been printed on RepRapPro’s own machines. Despite the fact that these machines are highly tuned RepRap 3D printers, some holes and features may need a little fettling to get the best performance from the RepRapPro Ormerod 2. There is a video how-to on fettling 3D printed parts here on Vimeo.
- Before you start the build, please ensure you have all the components as listed on the packing list included in the kit. If anything is missing or damaged, please contact us through our contact page.
- We understand that people may want to change aspects of the machine’s design, and in fact we encourage this as it is one of the benefits of open-source development. Before changing anything, please be aware that the RepRapPro Ormerod 2 has been designed to maximise its build volume relative to the the machine’s footprint, and as such many of its components fit closely to others. So consider your changes carefully before you try to implement them. And when you find improvements, please tell us and the world so that we can include them in future kits, and so that existing owners can upgrade their own machines.
- The RepRapPro Ormerod 2 is a robust RepRap machine once assembled; however it does require a certain amount of care during assembly. If in doubt, force is usually not the answer! There are many ways to get support and advice; see below.
## Ormerod 2 Versions
Some sections of the instructions are arranged in tabs, with alternate parts and instructions, depending on the version of your kit. Below is the changelog, which shows the differences between kit versions. The tabs refer to the version number of the Ormerod kit. Your Ormerod kit version number is marked on the sticker on the power supply (on 528.2 and later kits ), or on the x-rib (for earlier kits). Use the LATEST version number – some kits have the 528.2 PSU, but the 528.1 x-rib. Use the set of instructions that relate to your printer.

528.0	Sept 2014: Original shipping version of Ormerod 2.
528.1	Oct 2014: Changes to packing. Acrylic fan spacer replaces printed fan-duct and nozzle-duct.
528.2	Dec 2014: Change to supplied power supply, and added lasercut acrylic parts to mount Duet on new PSU.
528.3	Feb 2015: Changes to packing.
528.4	New heated bed design, new bed wiring loom.
528.5	Ships with new Quick-set nozzle. Separate hot end and fan looms. Cooling fan and duct supplied. Small updates to some printed parts (x-carriage, z-upper-mount, y-motor-mount). Changes to packing.

## Printing Parts for Ormerod 2
If you have bought the hardware-only version of the Ormerod 2 kit, you will want to print the parts. You may also want to print spare parts for your printer. The list below shows the part number, part name, quantity and location of the parts. Parts are available as STL and SolidWorks files, and there should also be a STEP assembly of the whole printer.
For Ormerod 2, part number 528.0 to 528.4, the easiest place to get the parts is here: https://github.com/reprappro/Ormerod/releases
For 528.5 onwards, we use the part number, rather than the name of the part, for the file name. For the latest version of the parts, which should be backwards compatible with all the previous versions, see the Ormerod github repository. Some parts common to all our machines are in the Library github repository.
You can download the whole github repository, or download the parts individually; the ‘Location’ in the link below links to the stl page. This will also help you identify the parts. If you download the parts individually, make sure you download the ‘RAW’ version of the file; if you right-click on a link and download, you will end up with a file with the right name (with .stl on the end), but it will actually be an html document!

#	Description	Qty	Location
547	y-idler-bracket	1	Ormerod/STLs
548	y-motor-bracket	1	Ormerod/STLs
469	z-motor-brace	1	Ormerod/STLs
437	z-lower-mount	1	Ormerod/STLs
438	z-upper-mount	1	Ormerod/STLs
527	z-corner-bracket	1	Ormerod/STLs
503	z-foot	1	Ormerod/STLs
549	y-bearing-belt-clamp	1	Ormerod/STLs
550	y-bearing-clamp-tagged	1	Ormerod/STLs
462	x-idler-bracket	1	Ormerod/STLs
546	x-carriage	1	Ormerod/STLs
501	nozzle-mount (one-piece nozzle, 528.4 and before)	1	Ormerod/STLs
1079	nozzle-mount (Quick-set nozzle, 528.5 onwards)	1	Ormerod/STLs
473	x-motor-bracket	1	Ormerod/STLs
407	z-runner-mount	1	Ormerod/STLs
441	z-gear-driven	1	Ormerod/STLs
440	z-gear	1	Ormerod/STLs
492	z-bearing-clamp	2	Ormerod/STLs
425	z-nut-trap	1	Ormerod/STLs
554	Extruder drive block	1	Ormerod/STLs
446	Extruder small gear	1	Ormerod/STLs
447	Extruder large gear	1	Ormerod/STLs
152	Tongue	1	Library/STLs
820	PSU cover	1	Library/STLs
821	PSU brace	1	Ormerod/STLs
442	Spool spigot	1	Ormerod/STLs
525	Spool clip	1	Ormerod/STLs
1123	Cooling fan duct	1	Ormerod/STLs

## Get Support
If you find you need help or advice with assembling, commissioning or using your RepRapPro Ormerod 2 3d printer, you can use the following channels:
- Check the instructions again; we are regularly updating them with feedback from our growing user-base.
- Contact the support department of the company that sold you your printer.
- Check the RepRap community forum, Ormerod section.
- Contact us on our irc (internet relay chat) channel RepRapPro on freenode irc
- Contact us via email; see our contact page.
## Archived Documents for Older Versions
If you have an older RepRapPro Ormerod and want a past copy of this documentation see these links:
RepRapPro Ormerod 1 Instructions
## Tool List
Tools required for the build of the RepRapPro Ormerod 2 3D printer:
### Required
Allen keys: 1.5mm, 2mm, 2.5mm, 4mm (the long reach type, with a ‘ball’ hex on the end, are very useful)
- Medium, cross-head screwdriver
- 8mm (M5) socket and/or spanner
- 15cm adjustable spanner
- Fine tweezers
- Ruler, at least 300mm
- Fine-nosed pliers
- Scissors
- Drill: 2mm
- Hand chuck, pin vice or small electric drill
- Small, flat-bladed, electrical screwdriver
- Pencil sharpener
- Digital Multimeter
- Hot air gun, or cigarette lighter (or other heat source such as a gas cooker ring for heating PTFE heatshrink; a hair dryer is not sufficient)
### For Adjusting Plastic Parts, if Necessary
- Drills: 3mm, 4mm
- File
- Half round needle file
- Sharp craft knife
### Nice to Have, But Not Necessary
# 5.5mm (M3) socket and/or spanner
- Vernier or digital callipers
# Y Axis Assembly
## Y axis sub-assemblies
### Y-idler-end
TIP: There’s a list of the Ormerod printed parts on THIS PAGE. Click on the ‘Location’, to see a preview of the printed part, if you’re not sure what it is.

#	Component	Qty	Type
	y-idler-bracket	1	Printed
	y-axis-end-plate ‘A’	1	Lasercut
	M4x12mm countersunk socket head screw	1	Fastener
	M4 T-nut	1	Fastener
	M3x12mm countersunk socket head screw	2	Fastener
	M3 Nut	2	Fastener
	M3x12mm cap head screw	1	Fastener
	623 bearing (10mm diameter)	1	Fastener

TIP: Click on pictures in the instructions to see a larger version. Right-click and select ‘Open link in new Tab’ to see the full size image.

Fit the 623 idler bearing to the y-idler-end. It may require a fair bit of force to push the bearing into position. It is held in place by a M3x12mm cap head screw. This should self-tap into the printed part, with no need for a nut on the free end.
Using the M3x12mm countersunk socket head screws, assemble the y-axis-end-plate ‘A’ with the y-motor-bracket, with an M3 nut on the back of each screw.
The M4x12mm countersunk socket-head screw goes through the y-idler-mount as shown, with the T-nut on the other side. Leave the T-nut loose – it connects with the aluminium extrusion.

### Y-motor-end
#	Component	Qty	Type
	y-motor-bracket	1	Printed
	y-axis-end-plate ‘B’	1	Lasercut
	M4x12mm countersunk socket head screw	1	Fastener
	M4 T-nut	1	Fastener
	M3x12mm countersunk socket head screw	2	Fastener
	M3 Nut	2	Fastener

Begin by assembling the Y-motor-end. Use y-axis-end-plate ‘B’ (there is a small ‘B’ engraved on one side of the plate) with the y-motor-bracket. As the y-axis-end-plate is laser-cut acrylic, the 12mm holes will be slightly larger in diameter on one side of the y-axis-end-plate (the side with the letter ‘B’) which will make it easier to insert the 12mm ground steel bar later.
Using the M3x12mm countersunk socket-head screws, connect the two parts together as shown, with an M3 nut on the back of each..
The M4x12mm countersunk socket-head screw goes through the y-motor-mount as shown, with the T-nut on the other side. Leave the T-nut loose – it connects with the aluminium extrusion.

## Y axis frame
The next step is to assemble the Y axis frame. For this you will need the following:

#	Component	Qty	Type
	y-motor-end	1	Assembled
	y-idler-end	1	Assembled
	Aluminium extrusion	1	Hardware
	Smooth rod 12x350mm	2	Hardware
	LM12UU Linear bearing	3	Hardware
	M6x16mm countersunk socket head screw	4	Fastener

#	Component	Qty	Type
	y-motor-end	1	Assembled
	y-idler-end	1	Assembled
	Aluminium extrusion	1	Hardware
	Smooth rod 12x350mm	2	Hardware
	LM12UU Linear bearing	3	Hardware
	M6x16mm countersunk socket head screw	4	Fastener

Screw the y-idler-end onto the aluminium extrusion, using two M6x16mm countersunk socket screws. These screws need to be tight – if they are loose, the Y-ends will move in relation to the aluminium extrusion, and the X axis will not be level to the bed.
On the inside of the y-idler-end, check that the M4 T-nut is located in the extrusion slot.
As you tighten the screw, the T-nut should rotate 90 degrees in the extrusion, from horizontal to vertical. It may need a little help! If it can’t rotate, it may have started too close to the printed part; loosen the screw off a couple of turns, then try tightening again. Once it has rotated so that it is vertical, fully tighten the screw.
With the y-idler-end supported by the edge of a table, take one of the 12x350mm smooth rods and push it into the hole in the acrylic end piece that is closest to the aluminium extrusion. The 12mm diameter holes are sized to be an interference fit with the rods, and the Acrylic laser cut plates are quite brittle so care must be taken when inserting the rods not to break the end plates. You can use a piece of wood, or soft-faced hammer, to tap gently on the end of the rod, if necessary.
NOTE: Some 12x350mm smooth rods may be a little longer, due to variability in manufacture. The y-idler-end printed part can accommodate this, with a pocket. The other places that the rods are used can similarly accommodate these rods (Z axis), or it doesn’t matter (X axis, Y axis front rod) – the longer rod will simply poke out the end a millimetre or so.
With the acrylic supported, push the second 12x350mm smooth rod into the hole in the end of the plate. Keep the rod perpendicular to the plate whilst pushing. Try to keep both rods upright, so they do not stress the holes in the Acrylic.
Slide the LM12UU Linear bearings onto the smooth rod. Put two onto the rod closest to the aluminium extrusion, and one on the front rod. Check they slide smoothly and freely.
Push the y-motor-end onto the smooth rods at the other end. This may be easiest with the Y axis vertical. Make sure the acrylic part is supported when pushing the rods in. Try and keep the smooth rods as straight as possible, to avoid damaging the acrylic parts. Push them home, so that the motor mount is flush with the aluminium extrusion. Again, only tap them in with a piece of wood, or soft-face hammer, to avoid damaging the parts.
Screw the y-motor-end onto the aluminium extrusion, using two M6x16mm countersunk socket screws. These screws need to be tight – if they are loose, the X axis will not be level to the bed.
Ensure the M4 T-nut is located in the extrusion slot, and tighten.
The completed assembly. Check all screws are tight.

## Y Axis Motor
Now you can fit the Y axis motor. For this step you will need the following:
#	Component	Qty	Type
	y-axis-frame	1	Assembled
	NEMA17 stepper motor	1	Hardware
	M3x8mm countersunk socket screw	2	Fasteners
	M3x40mm cap head screw	1	Fasteners
	M3 washer	1	Fasteners

One screw needs to be removed from the back of the motor, as shown. Don’t lose this M3x26mm crosshead screw; we’ll be using it for the y-carriage.
Fit the motor into the printed y-motor-bracket. Secure the motor in place with 2 x M3x8mm countersunk socket screws in the front face.
Put one M3x40mm cap head screw with an M3 washer, in the back of the motor, where you took out the motor screw.
The three screws of the motor are mounted in slots, so you can slide the motor a small distance. This allows you to adjust the belt tension, once the belt is fitted. Leave the screws hand tight with the motor at the right-hand end of the slots in the picture.
The completed y axis assembly.

# Z Axis Assembly

# Y Carriage

# X Axis Assembly

# X Axis Mounting

# Heated Bed Assembly

# Extruder Drive Assembly

# Hot End Assembly – Quick-set

# Hot End Assembly

# Electronics

# Wiring

# Commissioning

# Calibration

# Printing

# Maintenance

# Troubleshooting